## Slide 1: Cairo BRT Western Corridor design
April 2021
GUC

## Slide 2: Cairo traffic congestion
Source: Google images
Notes: tab3n e7na kolena 3la deraya bel sowar dy w benwagh el wake3 dh kol youm
Traffic congestion and how its affecting us: za7met el mrour wel khathafa el mororeya el 3alya ba2et ta2asr 3alina be shakl fa3al
1)Longer Trip times إختناق السير ساعة الذروة wa2t el re7la ketr
2)Not enough time to do many activities أنشطةper day (Chart on how much people spend in traffic/day)
3)Pollution (Cairo levels of pollutions; if it exceeds WHO guidelines; if people are dying because of that every year)
4)Tiring; accordingly affects our productivity not working efficiently يؤثر على الإنتاجية بشكل فعال

## Slide 3: Most Public transport trips depends on microbuses
Modernized public transport buses
78 km metro network
Minibus – 26 seats
Microbus - 14 seats

## Slide 4: Cairo BRT Master Plan
Year | Population | Metro (km) | BRT phase | BRT (km) | BRT fleet* | Total MRT (km) | RTR
2018 | 20,000,000 | 74 | Existing | 0 | 0 | 74 | 4
2021 | 21,000,000 | 74 | 1a | 67 | 538 | 141 | 7
2023 | 23,000,000 | 74 | 1b | 115 | 917 | 188 | 8
2028 | 26,000,000 | 131 | 2 | 251 | 2,011 | 382 | 15
2033 | 29,000,000 | 131 | 3 | 415 | 3,323 | 546 | 19
Year 2033
6th of October City
Cairo
New Cairo
Giza
Notes: Rapid Transit to Resident Ratio
Alignment of existing CTA & paratransit routes
Public transport passenger volumes (where counts are available)
Integration with existing and planned metro corridors
Available street right-of-way
Links to development areas (e.g., New Capital)
Bus Operational Plan in NCC and BRT in 6th of Oct.

## Slide 5: Cairo BRT Western Corridor
Giza
6th of October City
41.5 km corridor
34 stations
3 terminals: Giza Square, Metro Faisal, & Industrial Rd
1 depot: Industrial Rd

## Slide 6: Planning process
  Mapping of existing public transport routes
Corridor identification
Passenger demand assessment
Infrastructure design
Service plan
Financial model
Business & institutional plan
Notes: Last two steps inconcurrent
تقييم الطلب على الركاب
Coding of CTA, minibus, and microbus routes using Transcad & Emme
- 103 routes surveyed (2018) + around 87 routes (2019)
- Routes not surveyed don’t interact with corridor and low frequency

## Slide 7: Data collection process
Available right of way
Boardings/ alightings
Public transport volumes
Public transport speeds
Notes: data collection process that informed the service plan

## Slide 8: Service plan - Western BRT
Line 1
39 km
97 min
28 stops
Line 3
26 km
59 min
9 stops
Line 2
38 km
93 min
24 stops
Line 4
10 km
27 min
11 stops
Daily boardings: 126,000 (express and regular services)
Speed: 21-35 km/h (vs. speed of 5-10 km/hr on Mehwar Markazi & Faisal today)
Stations: 34
Fleet: 119 articulated buses (18 m bus)
Notes: *Ticket price : 4.5, 6.5, 8.5 EGP

## Slide 9: Planning process
  Station configuration based on passenger demand
Corridor identification
Passenger demand assessment
Infrastructure design
Service plan
Financial Model
Business & Institutional Mod.

## Slide 10: Al Mehwar Al Markazi Cross section on stations
Design Criteria
Bi-directional with at-grade pedestrian crossing station
Station with 2 platforms per direction on higher demand stations
Uses central median for stations
Eliminates service road on narrow stretches (stations), except on wider sections
9.00
3.00
2.00
3.00
2.00
9.00

## Slide 11: Al Mehwar Al Markazi Cross section outside stations
Design Criteria
Parking spaces out of the station areas
Median of 5,5 meters is preserved
2.50
3.00
2.00
2.50
3.00
2.00

## Slide 12: Station typologies
Number of stations | Station Typology | Station Type
1 | Bidirectional with Pedestrian Bridge (2 platform per direction) | A
7 | Bidirectional At-Grade (1 platform per direction) | B
3 | Bidirectional with Pedestrian Bridge (1 platform per direction) | C
9 | Staggered with Pedestrian Bridge (1 platform per direction) | D
3 | Staggered with Pedestrian Bridge (2 platform per direction) | E
2 | Staggered At-Grade (1 platform per direction) | F
1 | Staggered At-Grade (1 platform per direction) | F*
2 | Staggered At-Grade (2 platform per direction) | G1
1 | Staggered At-Grade (2 platform per direction) | G2
2 | Bidirectional At-Grade (2 platform per direction) | H1
1 | Bidirectional At-Grade (2 platform per direction) | H2
1 | Staggered At-Grade (2 platform per direction) | J
1 | Bidirectional At-Grade (2 platform per direction) | K

## Slide 13: Type H1: At-grade station
(Type H1)
Elevation view
Plan view

## Slide 14: At-grade station
Station entrance
Station interior
Station view

## Slide 15: Type D: Pedestrian bridge station
Station render
Plan view
Elevation view

## Slide 16: Station-bus interface
High ceiling with partial roof cover over bus
Platform extension (200 mm) to ensure safe distance between bus and station
Minimal gap for easy boarding (< 50 mm)
Platform and bus floor at same level (e.g. 900 mm)

## Slide 17: Bus specifications
Articulated: 140 passengers
Specifications:
Articulated
Length of 18 m
Four left doors
Engine emission technology
  Euro III or superior
Air Conditioning
High floor

## Slide 18
Faisal Street - existing

## Slide 19
Faisal Street - proposed

## Slide 20
Bridge/Tunnel | Activity
1 | Bridge to Faisal Metro Station and Giza Terminal
2 | Bridge from Mansoureya to Faisal
3 | Tunnel at Old Fayoum x New Fayoum
4 | Tunnel at Wahat x Old Fayoum road
5 | Bridge 4 (Wahat x 26th of July)
6 | Dolphin Bridge (Mehwar Markazi x 26th of July)
7 | Depot Bridge
BRT bridges and tunnels
1
2
3
4
5
6
7

## Slide 21: 26th of July Intersection Existing

## Slide 22: 26th of July Intersection Alternative 1 with BRT crossing at grade

## Slide 23: 26th of July Intersection Alternative 2 with BRT exclusive flyover
*From Al Mehwar Al Markazi to 26th of July north, currently vehicles use the U-Turn. The solution proposed allows the left turn directly with traffic lights

## Slide 24: Giza Bridges
Metro Faisal BRT Terminal
Giza Square BRT Terminal

## Slide 25: Industrial Rd. Depot

## Slide 26: Planning process
Passenger
$ fare
Trust Fund
Fare Collection Company
Bus Operator Company
$ remuneration
$ fare revenue
$ remuneration
$ subsidy
Government
$ remuneration
Corridor identification
Passenger demand assessment
Infrastructure design
Service plan
Financial Model
Business & Institutional Mod.

## Slide 27: Planning process
Corridor identification
Passenger demand assessment
Infrastructure design
Service plan
Financial Model
Business & Institutional Mod.

## Slide 28
africa.itdp.org
Thank you